Connecting Picaxe to Cayenne using Raspberry Pi and MQTT.

Abstract:
Picaxe can be used as a cheap way to collect data from a varitity of places, however viewing that data is not always the most easy task. This document with accomanying scripts explains how to connect a picaxe receiver to a Raspberry Pi and then use the provided scripts with minimal configuration to upload the data to Cayenne where it can be viewed online in real time. The collecting of the data is beyond the scope of this document, as is the transmission from collecting picaxe to receiver picaxe.

Setup:
The Picaxe should needs to connected to the Raspberry Pi's GND and UART_RX pins. It could also be connected to the 5v pin so that the picaxe needant rely on batteries.

For best results insert a fresh install of Raspberrian into the Raspberry Pi. To install this download the Raspberrian disk image here:
https://www.raspberrypi.org/downloads/raspbian/
For creating the bootable sd card on Windows see this guide:
https://www.raspberrypi.org/documentation/installation/installing-images/windows.md
For creating the bootage sd card on MacOS see this guide:
https://www.raspberrypi.org/documentation/installation/installing-images/mac.md
For creating the bootable sd card on Linux use the dd tool, CAREFULLY:
First run fdisk -l and look for the path to the usb device, it will look something like /dev/sdX
Run sudo dd if=raspberrian_lastest.img of=/dev/sdX
Warning, getting the wrong devices can destroy your hard drive. This goes with any operating system but can be very easy to do using the dd tool so be extra careful.
Insert the SD card and boot the Raspberry Pi, clone this repostiary:

Run setup_helper.sh